## Slide 1: GPU Architecture
A Collaboration Between
David Kaeli, Northeastern University
Benedict R. Gaster, AMD
© 2011

## Slide 2: Instructor Notes
We describe motivation for talking about underlying device architecture because device architecture is often avoided in conventional programming courses
Contrast conventional multicore CPU architecture with high level view of AMD and Nvidia GPU Architecture
This lecture starts with a high level architectural view of all GPUs, discusses each vendor’s architecture and then converges back to the OpenCL spec
  Stress on the difference between the AMD VLIW architecture and Nvidia scalar architecture
  Also discuss the different memory architecture
Brief discussion of ICD and compilation flow of OpenCL provides a lead to Lecture 5 where the first complete OpenCL program is written

## Slide 3: Topics
Mapping the OpenCL spec to many-core hardware
  AMD GPU Architecture
  Nvidia GPU Architecture
  Cell Broadband Engine
OpenCL Specific Topics
  OpenCL Compilation System
  Installable Client Driver (ICD)

## Slide 4: Motivation
Why are we discussing vendor specific hardware if OpenCL is platform independent ?
  Gain intuition of how a program’s loops and data need to map to OpenCL kernels in order to obtain performance
  Observe similarities and differences between Nvidia and AMD hardware
  Understanding hardware will allow for platform specific tuning of code in later lectures
Notes: This point is important because this would be a common question while teaching an open platform agnostic programming

## Slide 5: Conventional CPU Architecture
Space devoted to control logic instead of ALU
CPUs are optimized to minimize the latency of a single thread
  Can efficiently handle control flow intensive workloads
Multi level caches used to hide latency
Limited number of registers due to smaller number of active threads
Control logic to reorder execution, provide ILP and minimize pipeline stalls
Conventional CPU Block Diagram
Control Logic
ALU
L1 Cache
L2 Cache
L3 Cache
~ 25GBPS
System Memory
A present day multicore CPU could have more than one ALU ( typically < 32) and some of the cache hierarchy is usually shared across cores
Notes: Basic computer architecture points for multicore CPUs

## Slide 6: Modern GPGPU Architecture
Generic many core GPU
  Less space devoted to control logic and caches
  Large register files to support multiple thread contexts
Low latency hardware managed thread switching
Large number of ALU per “core” with small user managed cache per core
Memory bus optimized for bandwidth
  ~150 GBPS bandwidth allows us to service a large number of ALUs simultaneously
On Board System Memory
High Bandwidth
bus to ALUs
Simple ALUs
Cache
Notes: High level 10,000 feet view of what a GPU looks like, irrespective of whether its AMD’s or Nvidia’s

## Slide 7: AMD GPU Hardware Architecture
AMD 5870 – Cypress
20 SIMD engines
16 SIMD units per core
5 multiply-adds per functional unit (VLIW processing)
2.72 Teraflops Single Precision
544 Gigaflops Double Precision
Source: Introductory OpenCL SAAHPC2010, Benedict R. Gaster
Notes: Very AMD specific discussion of low-level GPU architecture

## Slide 8: SIMD Engine
A SIMD engine consists of a set of “Stream Cores”
Stream cores arranged as a five way Very Long Instruction Word (VLIW) processor
  Up to five scalar operations can be issued in a VLIW instruction
  Scalar operations executed on each processing element
Stream cores within compute unit execute same VLIW instruction
  The block of work-items that are executed together is called a wavefront.
  64 work items for 5870
One SIMD Engine
Source: AMD Accelerated Parallel Processing OpenCL Programming Guide
General Purpose Registers
One Stream Core
T-Processing
Element
Branch
Execution Unit
Processing
Elements
Instruction and Control Flow
Notes: Very AMD specific discussion of low-level GPU architecture
Discusses a single SIMD engine and the stream cores

## Slide 9: AMD Platform as seen in OpenCL
Individual work-items execute on a single processing element
Processing element refers to a single VLIW core
Multiple work-groups execute on a compute unit
A compute unit refers to a SIMD Engine
Notes: We converge back to the OpenCL terminology to understand how the AMD GPU maps onto the OpenCL processing elements

## Slide 10: AMD GPU Memory Architecture
Memory per compute unit
  Local data store (on-chip)
  Registers
  L1 cache (8KB for 5870) per compute unit
L2 Cache shared between compute units (512KB for 5870)
Fast path for only 32 bit operations
Complete path for atomics and < 32bit operations
SIMD Engine
LDS, Registers
Compute Unit to Memory X-bar
LDS
L1 Cache
L2 Cache
Write Cache
Atomic Path
Notes: A brief overview of the AMD GPU memory architecture (As per Evergreen Series)

## Slide 11: AMD Memory Model in OpenCL
Subset of hardware memory exposed in OpenCL
Local Data Share (LDS) exposed as local memory
  Share data between items of a work group designed to increase performance
  High Bandwidth access per SIMD Engine
Private memory utilizes registers per work item
Constant Memory
  __constant tags utilize L1 cache.
Global Memory
Private
Memory
Workitem 1
Private
Memory
Workitem 1
Compute Unit 1
Local Memory
Global / Constant Memory Data Cache
Local Memory
Private
Memory
Workitem 1
Private
Memory
Workitem 1
Compute Unit N
Compute Device
Compute Device Memory
Notes: The mapping of the AMD GPU memory components to the OpenCL terminology.
Architecturally this is similar for AMD and Nvidia except that each ones have their own vendor specific names
Similar types of memory are mapped to local memory for both AMD and Nvidia

## Slide 12: AMD Constant Memory Usage
Constant Memory declarations for AMD GPUs only beneficial for following access patterns
  Direct-Addressing Patterns: For non array constant values where the address is known initially
  Same Index Patterns: When all work-items reference the same constant address
  Globally scoped constant arrays: Arrays that are initialized, globally scoped can use the cache if less than 16KB
  Cases where each work item accesses different indices, are not cached and deliver the same performance as a global memory read
Source: AMD Accelerated Parallel Processing OpenCL Programming Guide
Notes: Summary of the usage of constant memory.
Important because there are a restricted set of cases where there is a hardware provided performance boost while using constant memory
This will have greater context with a complete example which would have to be later.
This slide is added in case some one is reading this while optimizing some application and needs device specific details

## Slide 13: Nvidia GPUs - Fermi Architecture
GTX 480 - Compute 2.0 capability
  15 cores or Streaming Multiprocessors (SMs)
  Each SM features 32 CUDA processors
  480 CUDA processors
Global memory with ECC
Source: NVIDIA’s Next Generation CUDA Architecture Whitepaper
Register File 32768 x 32bit
Warp Scheduler
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Dispatch Unit
Instruction Cache
LDST
LDST
LDST
LDST
LDST
LDST
LDST
LDST
LDST
LDST
LDST
LDST
LDST
LDST
LDST
LDST
SFU
SFU
SFU
SFU
Interconnect Memory
L1 Cache / 64kB Shared Memory
L2 Cache
Warp Scheduler
Dispatch Unit
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Dispatch Port
Operand Collector
FP Unit
Int Unit
Result Queue
CUDA Core
Notes: Nvidia “Fermi” Architecture, High level overview.

## Slide 14: Nvidia GPUs – Fermi Architecture
SM executes threads in groups of 32 called warps.
  Two warp issue units per SM
Concurrent kernel execution
  Execute multiple kernels simultaneously to improve efficiency
CUDA core consists of a single ALU and floating point unit FPU
Source: NVIDIA’s Next Generation CUDA Compute Architecture Whitepaper
Register File 32768 x 32bit
Warp Scheduler
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Dispatch Unit
Instruction Cache
LDST
LDST
LDST
LDST
LDST
LDST
LDST
LDST
LDST
LDST
LDST
LDST
LDST
LDST
LDST
LDST
SFU
SFU
SFU
SFU
Interconnect Memory
L1 Cache / 64kB Shared Memory
L2 Cache
Warp Scheduler
Dispatch Unit
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Dispatch Port
Operand Collector
FP Unit
Int Unit
Result Queue
CUDA Core
Notes: Architectural highlights of a SM in a Fermi GPU
Mention scalar nature of a CUDA core unlike AMD’s VLIW architecture

## Slide 15: SIMT and SIMD
SIMT denotes scalar instructions and multiple threads sharing an instruction stream
  HW determines instruction stream sharing across ALUs
  E.g. NVIDIA GeForce (“SIMT” warps), AMD Radeon architectures (“wavefronts”) where all the threads in a warp /wavefront proceed in lockstep
  Divergence between threads handled using predication
SIMT instructions specify the execution and branching behavior of a single thread
  SIMD instructions exposes vector width,
  E.g. of SIMD: explicit vector instructions like x86 SSE
Notes: The SIMT execution model of GPU threads. SIMD specifies vector width as in SSE.
However the SIMT execution model doesn’t necessarily need to know the number of threads in a warp for a OpenCL program.
The concept of a warp / wavefront is not within OpenCL.

## Slide 16: SIMT Execution Model
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
…
Wavefront
…
Cycle
SIMD Width
SIMD execution can be combined with pipelining
  ALUs all execute the same instruction
  Pipelining is used to break instruction into phases
    When first instruction completes (4 cycles here), the next instruction is ready to execute
Notes: The SIMT Execution mode which shows how different threads execute the same instruction

## Slide 17: Nvidia Memory Hierarchy
L1 cache per SM configurable to support shared memory and caching of global memory
  48 KB Shared / 16 KB of L1 cache
  16 KB Shared / 48 KB of L1 cache
Data shared between work items of a group using shared memory
Each SM has a 32K register bank
L2 cache (768KB) that services all operations (load, store and texture)
  Unified path to global for loads and stores
Shared Memory
L1 Cache
L2 Cache
Global Memory
Thread Block
Registers
Notes: Nvidia specific GPU memory architecture.
Main highlight is the configurable L1 : Shared size ratio
L2 is not exposed in the OpenCL specification

## Slide 18: Nvidia Memory Model in OpenCL
Like AMD, a subset of hardware memory exposed in OpenCL
Configurable shared memory is usable as local memory
  Local memory used to share data between items of a work group at lower latency than global memory
Private memory utilizes registers per work item
Global Memory
Private
Memory
Workitem 1
Private
Memory
Workitem 1
Compute Unit 1
Local Memory
Global / Constant Memory Data Cache
Local Memory
Private
Memory
Workitem 1
Private
Memory
Workitem 1
Compute Unit N
Compute Device
Compute Device Memory
Notes: Similar to AMD in the sense that low latency memory which is the shared memory becomes OpenCL local memory

## Slide 19: Cell Broadband Engine
Developed by Sony, Toshiba, IBM
Transitioned from embedded platforms into HPC via the Playstation 3
OpenCL drivers available for Cell Bladecenter servers
Consists of a Power Processing Element (PPE) and multiple Synergistic Processing Elements (SPE)
Uses the IBM XL C for OpenCL compiler
Source: http://www.alphaworks.ibm.com/tech/opencl
SPU
LS
SPU
LS
SPU
LS
SPU
LS
Element Interconnect ~ 200GBPS
L1 and L2 Cache
POWER PC
SPE 0
SPE 1
SPE 2
SPE 3
LS = Local store per SPE of 256KB
PPE
25 GBPS
25 GBPS
25 GBPS
Memory & Interrupt Controller
Notes: Brief introduction on the Cell

## Slide 20: Cell BE and OpenCL
Cell Power/VMX CPU used as a CL_DEVICE_TYPE_CPU
Cell SPU (CL_DEVICE_TYPE_ACCELERATOR)
  No. of compute units on a SPU accelerator device is <=16
  Local memory size <= 256KB
  256K of local storage divided among OpenCL kernel, 8KB global data cache, local, constant and private variables
OpenCL accelerator devices, and OpenCL CPU device share a common memory bus
Provides extensions like “Device Fission” and “Migrate Objects” to specify where an object resides (discussed in Lecture 10)
No support for OpenCL images, sampler objects, atomics and byte addressable memory
Source: http://www.alphaworks.ibm.com/tech/opencl
Notes: Brief overview of how the Cell’s memory architecture maps to OpenCL
For usage of the Cell in specific applications a high level view is given and Lec 10 discusses its special extensions
Optimizations in Lec 6-8 do not apply to the Cell because of its very different architecture

## Slide 21: An Optimal GPGPU Kernel
From the discussion on hardware we see that an ideal kernel for a GPU:
  Has thousands of independent pieces of work
    Uses all available compute units
    Allows interleaving for latency hiding
  Is amenable to instruction stream sharing
    Maps to SIMD execution by preventing divergence between work items
  Has high arithmetic intensity
    Ratio of math operations to memory access is high
    Not limited by memory bandwidth
Note that these caveats apply to all GPUs
Notes: Discusses an optimal kernel to show how irrespective of the different underlying architecture, an optimum program for both AMD and Nvidia would have similar characteristics

## Slide 22: OpenCL Compilation System
LLVM - Low Level Virtual Machine
Kernels compiled to LLVM IR
Open Source Compiler
  Platform, OS independent
  Multiple back ends
http://llvm.org
OpenCL Compute Program
LLVM IR
Nvidia PTX
AMD CAL IL
x86
LLVM Front-end
Notes: Explains how platform agnostic OpenCL code is mapped to a device specific Instruction Set Architecture.

## Slide 23: Installable Client Driver
ICD allows multiple implementations to co-exist
Code only links to libOpenCL.so
Application selects implementation at runtime
Current GPU driver model does not easily allow multiple devices across manufacturers
clGetPlatformIDs() and clGetPlatformInfo() examine the list of available implementations and select a suitable one
Application
libOpenCL.so
atiocl.so
Nvidia-opencl
Notes: The ICD is added in order to explain how we can interface different OpenCL implementations with a similar compilation tool-chain

## Slide 24: Summary
We have examined different many-core platforms and how they map onto the OpenCL spec
  An important take-away is that even though vendors have implemented the spec differently the underlying ideas for obtaining performance by a programmer remain consistent
We have looked at the runtime compilation model for OpenCL to understand how programs and kernels for compute devices are created at runtime
  We have looked at the ICD to understand how an OpenCL application can choose an implementation at runtime
Next Lecture
  Cover moving of data to a compute device and some simple but complete OpenCL examples