## Slide 1: Understanding GPU Memory
A Collaboration Between
David Kaeli, Northeastern University
Benedict R. Gaster, AMD
© 2011

## Slide 2: Instructor Notes
This lecture begins with an example of how a wide-memory bus is utilized in GPUs
The impact of memory coalescing and memory bank conflicts are also described along with examples on current hardware
This lecture is important because achieving high memory bandwidth is often the most important requirement for many GPU applications

## Slide 3: Topics
Introduction to GPU bus addressing
Coalescing memory accesses
Introduction to memory banks
Memory bank conflicts

## Slide 4: Example
  Array X is a pointer to an array of integers (4-bytes each) located at address 0x00001232
  A thread wants to access the data at X[0]
    int tmp = X[0];
0x00001232
X
0
1
2
3
4
5
6
7
0x00001232
0x00001236
0x00001248
.
.
.
.
.
.
.
Notes: This is the start of an example explaining how GPU’s wide memory buses work.

## Slide 5: Bus Addressing
Assume that the memory bus is 32-bytes (256-bits) wide
  This is the width on a Radeon 5870 GPU
The byte-addressable bus must make accesses that are aligned to the bus width, so the bottom 5 bits are masked off
Any access in the range 0x00001220 to 0x0000123F will produce the address 0x00001220
Desired address: | 0x00001232
Bus mask: | 0xFFFFFFE0
Bus access: | 0x00001220

## Slide 6: Bus Addressing
All data in the range 0x00001220 to 0x0000123F is returned on the bus
In this case, 4 bytes are useful and 28 bytes are wasted
?
?
?
0
1
2
3
4
0x00001220
Send an address
Receive data
0x00001220
Memory Controller
Desired element
Notes: The desired element is at 0x00001232 as shown 2 slides back.

## Slide 7: Coalescing Memory Accesses
To fully utilize the bus, GPUs combine the accesses of multiple threads into fewer requests when possible
Consider the following OpenCL kernel code:
Assuming that array X is the same array from the example, the first 16 threads will access addresses 0x00001232 through 0x00001272
If each request was sent out individually, there would be 16 accesses total, with 64 useful bytes of data and 448 wasted bytes
  Notice that each access in the same 32-byte range would return exactly the same data
int tmp = X[get_global_id(0)];

## Slide 8: Coalescing Memory Accesses
When GPU threads access data in the same 32-byte range, multiple accesses are combined so that each range is only accessed once
  Combining accesses is called coalescing
For this example, only 3 accesses are required
  If the start of the array was 256-bit aligned, only two accesses would be required
?
?
?
0
1
2
3
4
0x00001220
5
6
7
8
9
10
11
12
0x00001240
13
14
15
?
?
?
?
?
0x00001260

## Slide 9: Coalescing Memory Accesses
Recall that for AMD hardware, 64 threads are part of a wavefront and must execute the same instruction in a SIMD manner
For the AMD 5870 GPU, memory accesses of 16 consecutive threads are evaluated together and can be coalesced to fully utilize the bus
  This unit is called a quarter-wavefront and is the important hardware scheduling unit for memory accesses

## Slide 10: Coalescing Memory Accesses
Global memory performance for a simple data copying kernel of entirely coalesced and entirely non-coalesced accesses on an ATI Radeon 5870
Chart: Data Size (MB)
| 1 | 4 | 16 | 32 | 64 | 128 | 256
Coalesced | 88.7784 | 110.0352 | 115.7407 | 117.4812 | 118.4834 | 118.8213 | 118.3432
Uncoalesced | 16.9837 | 17.8776 | 7.1282 | 8.6147 | 10.4716 | 9.4347 | 8.5615

## Slide 11: Coalescing Memory Accesses
Global memory performance for a simple data copying kernel of entirely coalesced and entirely non-coalesced accesses on an NVIDIA GTX 285
Chart: Data Size (MB)
| 1 | 4 | 16 | 32 | 64 | 128 | 256
Coalesced | 42.4592 | 88.7784 | 104.1667 | 110.2293 | 110.7174 | 111.8568 | 112.2334
Uncoalesced | 6.0282 | 7.032 | 7.2021 | 7.0343 | 7.1584 | 7.209 | 7.2237

## Slide 12: Memory Banks
Memory is made up of banks
  Memory banks are the hardware units that actually store data
The memory banks targeted by a memory access depend on the address of the data to be read/written
  Note that on current GPUs, there are more memory banks than can be addressed at once by the global memory bus, so it is possible for different accesses to target different banks
    Bank response time, not access requests, is the bottleneck
Successive data are stored in successive banks (strides of 32-bit words on GPUs) so that a group of threads accessing successive elements will produce no bank conflicts

## Slide 13: Bank Conflicts – Local Memory
Bank conflicts have the largest negative effect on local memory operations
  Local memory does not require that accesses are to sequentially increasing elements
Accesses from successive threads should target different memory banks
  Threads accessing sequentially increasing data will fall into this category

## Slide 14: Bank Conflicts – Local Memory
On AMD, a wavefront that generates bank conflicts stalls until all local memory operations complete
  The hardware does not hide the stall by switching to another wavefront
The following examples show local memory access patterns and whether conflicts are generated
  For readability, only 8 memory banks are shown

## Slide 15: Bank Conflicts – Local Memory
If there are no bank conflicts, each bank can return an element without any delays
  Both of the following patterns will complete without stalls on current GPU hardware
0
1
2
3
4
5
6
7
Memory Bank
0
1
2
3
4
5
6
7
Thread
0
1
2
3
4
5
6
7
Memory Bank
0
1
2
3
4
5
6
7
Thread

## Slide 16: Bank Conflicts – Local Memory
If multiple accesses occur to the same bank, then the bank with the most conflicts will determine the latency
  The following pattern will take 3 times the access latency to complete
0
1
2
3
4
5
6
7
Memory Bank
0
1
2
3
4
5
6
7
Thread
2
1
3
1
1
Conflicts

## Slide 17: Bank Conflicts – Local Memory
If all accesses are to the same address, then the bank can perform a broadcast and no delay is incurred
  The following will only take one access to complete assuming the same data element is accessed
0
1
2
3
4
5
6
7
Memory Bank
0
1
2
3
4
5
6
7
Thread

## Slide 18: Bank Conflicts – Global Memory
Bank conflicts in global memory rely on the same principles, however the global memory bus makes the impact of conflicts more subtle
  Since accessing data in global memory requires that an entire bus-line be read, bank conflicts within a work-group have a similar effect as non-coalesced accesses
    If threads reading from global memory had a bank conflict then by definition it manifest as a non-coalesced access
    Not all non-coalesced accesses are bank conflicts, however
The ideal case for global memory is when different work-groups read from different banks
  In reality, this is a very low-level optimization and should not be prioritized when first writing a program

## Slide 19: Summary
GPU memory is different than CPU memory
  The goal is high throughput instead of low-latency
Memory access patterns have a huge impact on bus utilization
  Low utilization means low performance
Having coalesced memory accesses and avoiding bank conflicts are required for high performance code
Specific hardware information (such as bus width, number of memory banks, and number of threads that coalesce memory requests) is GPU-specific and can be found in vendor documentation