## Slide 1: GPU Threads and Scheduling
A Collaboration Between
David Kaeli, Northeastern University
Benedict R. Gaster, AMD
© 2011

## Slide 2: Instructor Notes
This lecture deals with how work groups are scheduled for execution on the compute units of devices
Also explain the effects of divergence of work items within a group and its negative effect on performance
Reasons why we discuss warps and wavefronts because even though they are not part of the OpenCL specification
  Serve as another hierarchy of threads and their implicit synchronization enables interesting implementations of algorithms on GPUs
  Implicit synchronization and write combining property in local memory used to implement warp voting
  We discuss how predication is used for divergent work items even though all threads in a warp are issued in lockstep

## Slide 3: Topics
Wavefronts and warps
Thread scheduling for both AMD and NVIDIA GPUs
Predication
Warp voting and synchronization
Pitfalls of wavefront/warp specific implementations

## Slide 4: Work Groups to HW Threads
OpenCL kernels are structured into work groups that map to device compute units
Compute units on GPUs consist of SIMT processing elements
Work groups automatically get broken down into hardware schedulable groups of threads for the SIMT hardware
  This “schedulable unit” is known as a warp (NVIDIA) or a wavefront (AMD)
Notes: A recap of how work groups are scheduled on GPUs

## Slide 5: Work-Item Scheduling
Hardware creates wavefronts by grouping threads of a work group
  Along the X dimension first
All threads in a wavefront execute the same instruction
  Threads within a wavefront move in lockstep
Threads have their own register state and are free to execute different control paths
  Thread masking used by HW
  Predication can be set by compiler
0,0
0,1
0,14
0,15
1,0
1,1
1,14
1,15
2,0
2,1
2,14
2,15
3,0
3,1
3,14
3,15
Wavefront 0
Wavefront 1
4,0
4,1
4,14
4,15
7,0
7,1
7,14
7,15
Wavefront 2
Wavefront 3
Grouping of work-group into wavefronts
Notes: Splitting of threads in a work group into wavefronts
Warp is a term based from CUDA terminology, while wavefront is a AMD term.

## Slide 6: Wavefront Scheduling - AMD
Wavefront size is 64 threads
  Each thread executes a 5 way VLIW instruction issued by the common issue unit
A Stream Core (SC) executes one VLIW instruction
  16 stream cores execute 16 VLIW instructions on each cycle
A quarter wavefront is executed on each cycle, the entire wavefront is executed in four consecutive cycles
SC 0
SC 2
SC 1
SC 3
SC 4
SC 15
Issue and Branch Control Unit
Local Data Share
SIMD Engine
Notes: Wavefront Scheduling - AMD

## Slide 7: Wavefront Scheduling - AMD
In the case of Read-After-Write (RAW) hazard, one wavefront will stall for four extra cycles
  If another wavefront is available it can be scheduled to hide latency
  After eight total cycles have elapsed, the ALU result from the first wavefront is ready, so the first wavefront can continue execution
Two wavefronts (128 threads) completely hide a RAW latency
  The first wavefront executes for four cycles
  Another wavefront is scheduled for the next four cycles
  The first wavefront can then run again
Note that two wavefronts are needed just to hide RAW latency, the latency to global memory is much greater
  During this time, the compute unit can process other independent wavefronts, if they are available
Notes: Effect of wavefront scheduling.
As seen in AMD hardware at least 2 wavefronts should always be actives

## Slide 8: Warp Scheduling - Nvidia
Work groups are divided into 32-thread warps which are scheduled by a SM
On Nvidia GPUs half warps are issued each time and they interleave their execution through the pipeline
The number of warps available for scheduling is dependent on the resources used by each block
Similar to wavefronts in AMD hardware except for size differences
Streaming Multiprocessor
SP
SP
SP
SP
Instruction Fetch/Dispatch
Shared Memory
SP
SP
SP
SP
Warp 0
Warp 1
Warp 2
t0 – t31
t32 – t63
t64 – t95
Work Group
Notes: Wavefront Scheduling - Nvidia

## Slide 9: Occupancy - Tradeoffs
Local memory and registers are persistent within compute unit when other work groups execute
  Allows for lower overhead context switch
The number of active wavefronts that can be supported per compute unit is limited
  Decided by the local memory required per workgroup and register usage per thread
The number of active wavefronts possible on a compute unit can be expressed using a metric called occupancy
Larger numbers of active wavefronts allow for better latency hiding on both AMD and NVIDIA hardware
Occupancy will be discussed in detail in Lecture 08
Notes: Benefits of having multiple warps active at a time include better latency hiding

## Slide 10: Divergent Control Flow
Instructions are issued in lockstep in a wavefront /warp for both AMD and Nvidia
However each work item can execute a different path from other threads in the wavefront
If work items within a wavefront go on divergent paths of flow control, the invalid paths of a work-items are masked by hardware
Branching should be limited to a wavefront granularity to prevent issuing of wasted instructions
Notes: Introducing divergent control flow

## Slide 11: Predication and Control Flow
How do we handle threads going down different execution paths when the same instruction is issued to all the work-items in a wavefront ?
Predication is a method for mitigating the costs associated with conditional branches
  Beneficial in case of branches to short sections of code
  Based on fact that executing an instruction and squashing its result may be as efficient as executing a conditional
  Compilers may replace “switch” or “if then else” statements by using branch predication
Notes: An introduction to predication.
A key point is that it is beneficial only for very short conditionals

## Slide 12: Predication for GPUs
Predicate is a condition code that is set to true or false based on a conditional
Both cases of conditional flow get scheduled for execution
  Instructions with a true predicate are committed
  Instructions with a false predicate do not write results or read operands
Benefits performance only for very short conditionals
Predicate = True for threads 0,2,4….
__kernel
void test() {
int tid= get_local_id(0) ;
if( tid %2 == 0)
Do_Some_Work() ;
else
Do_Other_Work() ;
}
Predicate = False for threads 1,3,5….
Predicates switched for the else condition
Notes: Predication example

## Slide 13: Divergent Control Flow
Case 1: All odd threads will execute if conditional while all even threads execute the else conditional. The if and else block need to be issued for each wavefront
Case 2: All threads of the first wavefront will execute the if case while other wavefronts will execute the else case. In this case only one out of if or else is issued for each wavefront
int tid = get_local_id(0)
if ( tid % 2 == 0) //Even Work Items
DoSomeWork()
else
DoSomeWork2()
int tid = get_local_id(0)
if ( tid / 64 == 0) //Full First Wavefront
DoSomeWork()
else if (tid /64 == 1) //Full Second Wavefront
DoSomeWork2()
Case 1
Case 2
  Conditional – With divergence
  Conditional – No divergence
Notes: Two different cases of divergence in a work group
Case1: Odd threads go down one path and even threads go down another path
Case2: Entire wavefront goes down a similar path

## Slide 14: Effect of Predication on Performance
T = tstart
T = tstart + t1 + t2
Do_Some_Work()
Do_Other _Work()
Time for Do_Some_Work = t1 (if case)
Time for Do_Other _Work = t2 (else case)
T = 0
Squash invalid results, invert mask
T = tstart + t1
Total Time taken = tstart +t1 + t2
t1
t2
if( tid %2 == 0)
Green colored threads have valid results
Squash invalid results
Green colored threads have valid results
Notes: When using predication, all threads go down all paths and using masks the invalid OP results are squashed
Time taken is simply sum of if and else block

## Slide 15: Warp Voting
Implicit synchronization per instruction allows for techniques like warp voting
  Useful for devices without atomic shared memory operations
  We discuss warp voting with the 256-bin Histogram example
For 64 bin histogram, we build a sub histogram per thread
Local memory per work group for 256 bins
  256 bins * 4Bytes * 64 threads / block = 64KB
  G80 GPUs have only 16KB of shared memory
Alternatively, build per warp subhistogram
Local memory required per work group
  256 bins * 4Bytes * 2 warps / block = 2KB
Shared memory write combining on allows ONLY one write from work-items i,j or k to succeed
work item i
work item k
Local memory
work item j
By tagging bits in local memory and rechecking the value a work-item could know if its previously attempted write succeeded
Notes: Warp voting can be implemented because of the implicit synchronization across work items is a warp
By using a per warp sub histogram, many work items within the active warp would attempt to increment the same location
All writes in such cases will not succeed because shared memory write combining on allows ONLY one write from a work-item to succeed
This necessitates warp voting

## Slide 16: Warp Voting for Histogram256
Build per warp subhistogram
  Combine to per work group subhistogram
  Local memory budget in per warp sub histogram technique allows us to have multiple work groups active
Handle conflicting writes by threads within a warp using warp voting
  Tag writes to per warp subhistogram with intra-warp thread ID
  This allows the threads to check if their writes were successful in the next iteration of the while loop
Worst case : 32 iterations done when all 32 threads write to the same bin
void addData256(
volatile __local uint * l_WarpHist,
uint data, uint workitemTag) {
unsigned int count;
do{
// Read the current value from histogram
count = l_WarpHist[data] & 0x07FFFFFFU;
// Add the tag and incremented data to
// the position in the histogram
count = workitemTag | (count + 1);
l_WarpHist[data] = count;
}
// Check if the value committed to local memory
// If not go back in the loop and try again
while(l_WarpHist[data] != count);
}
32 bit Uint
5 bit tag
27 bit tag
Source: Nvidia GPU Computing SDK Examples
Notes: Tag is checked on the next pass through the loop to check if the write was successful

## Slide 17: Pitfalls of using Wavefronts
OpenCL specification does not address warps/wavefronts or provide a means to query their size across platforms
  AMD GPUs (5870) have 64 threads per wavefront while NVIDIA has 32 threads per warp
  NVIDIA’s OpenCL extensions (discussed later) return warp size only for Nvidia hardware
Maintaining performance and correctness across devices becomes harder
  Code hardwired to 32 threads per warp when run on AMD hardware 64 threads will waste execution resources
  Code hardwired to 64 threads per warp when run on Nvidia hardware can lead to races and affects the local memory budget
  We have only discussed GPUs, the Cell doesn’t have wavefronts
Maintaining portability – assign warp size at JIT time
  Check if running AMD / Nvidia and add a –DWARP_SIZE Size to build command
Notes: Maintaining performance and correctness portability becomes harder with warp / wavefront constructs in your program

## Slide 18: Warp-Based Implementation
Implicit synchronization in warps at each instruction allows for expression of another thread hierarchy within work group
  Warp specific implementations common in CUDA literature
E.g.: 256 Bin Histogram
  NVIDIA’s implementation allows building histograms in local memory for devices without atomic operation support and limited shared memory
  Synchronization in warps allows for implementing the voting discussed previously reducing local memory budget from N_THREADS*256 to N_WARPS_PER_BLOCK*256
E.g.: CUDPP: CUDA Data Parallel Primitives
  Utilizes an efficient warp scan to construct a block scan which works on one block in CUDA
Notes: Lots of examples in the CUDA SDK use the notion of warps to either enforce some communication or reduce shared memory requirements

## Slide 19: Summary
Divergence within a work-group should be restricted to a wavefront/warp granularity for performance
A tradeoff between schemes to avoid divergence and simple code which can quickly be predicated
  Branches are usually highly biased and localized which leads to short predicated blocks
The number of wavefronts active at any point in time should be maximized to allow latency hiding
  Number of active wavefronts is determined by the requirements of resources like registers and local memory
Wavefront specific implementations can enable more optimized implementations and enables more algorithms to GPUs
  Maintaining performance and correctness may be hard due to the different wavefront sizes on AMD and NVIDIA hardware